## Slide 1: Unit-3 Combinational Digital Circuits
krunal.vyas@darshan.ac.in
9601901005
Computer Science & Engineering
Prof. Krunal D Vyas
Digital Fundamentals (DF)
DU #2301CS102

## Slide 2

Looping
Outline
  Multiplexer, De-Multiplexer
  Decoders, Encoders, Priority encoders
  Adders, Subtractors
  Digital Comparator
  Parity Generator
  Code Converters

## Slide 3: Multiplexer, De-Multiplexer
Section - 1

## Slide 4: Multiplexer
A multiplexer(MUX) is a device that allows digital information from several sources to be routed onto a single line for transmission over that line to a common destination.
Consider an integer ‘m’, which is constrained by the following relation:
m = 2n, where m and n are both integers.
A m-to-1 Multiplexer has
  m Inputs: I0, I1, I2, ................ I(m-1)
  One Output: Y
  n Control inputs: S0, S1, S2, ...... S(n-1)
  One (or more) Enable input(s)
Such that Y may be equal to one of the inputs, depending upon the control inputs.

## Slide 5: 4-to-1 Multiplexer
I0
I1
I2
I3
S0
S1
Y
1 output
n control inputs
2n inputs
Enable (G)
4 x 1 MUX
Select Inputs |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3
0
0
I0

## Slide 6: 4 x 1 MUX Actual Circuit
I3
I2
I1
I0
S0
S1
Enable (G)
Y

## Slide 7: Logic function generator using Multiplexer
Implement the following function using 8 to 1 MUX
F(x,y,z) =
S2 | S1 | S0 | F
x | y | z | 
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
z
y
x
1
1
1
1
0
0
0
0
Output = F

## Slide 8: Logic function generator using Multiplexer (Method)
Multiplexer with n-data select inputs can implement any function of n + 1 variables.
The first n variables of the function as the select inputs and to use the least significant input variable and its complement to drive some of the data inputs.
If the single variable is denoted by D, each data output of the multiplexer will be D, D’, 1, or 0.
Suppose, we wish to implement a 4-variable logic function using a multiplexer with three data select inputs.
Let the input variables be A, B, C, and D; D is the LSB.
A truth table for the function F(A, B, C, D) is constructed with ABC has the same value twice once with D = 0 and again with D = 1.

## Slide 9: Logic function generator using Multiplexer (Method)
The following rules are used to determine the connections that should be made to the data inputs of the multiplexer.
  If F = 0 both times when the same combination of ABC occurs, connect logic 0 to the data input selected by that combination.
  If F = 1 both times when the same combination of ABC occurs, connect logic 1 to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D in each case, connect D to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D’ in each case, connect D’ to the data input selected by that combination.

## Slide 10
Implement the following function using 8 to 1 MUX
F =
S2 | S1 | S0 | D | F | 
A | B | C |  |  | 
0 0 | 0 0 | 0 0 | 0 1 | 1 1 | F = 1
0 0 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
0 0 | 1 1 | 0 0 | 0 1 | 1 0 | F = D’
0 0 | 1 1 | 1 1 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
1 1 | 1 1 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 1 1 | 1 1 | 0 1 | 1 1 | F = 1
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
C
B
A
1
D’
0
1
1
0
0
1
Output = F

## Slide 11: Demultiplexer
A demultiplexer(DEMUX) is a device that allows digital information from one source to be routed onto a multiple lines for transmission over different destinations.
Consider an integer ‘m’, which is constrained by the following relation:
m = 2n, where m and n are both integers.
A 1-to-m Demultiplexer has
  One Input: D
  m Outputs: O0, O1, O2, ................ O(m-1)
  n Control inputs: S0, S1, S2, ...... S(n-1)
  One (or more) Enable input(s)
Such that D may be transfer to one of the outputs, depending upon the control inputs.

## Slide 12: 1-to-4 Demultiplexer
D
O0
O1
O2
O3
1x4 DEMUX
S1
S0
Select code |  | Outputs |  |  | 
S1 | S0 | O3 | O2 | O1 | O0
0 | 0 | 0 | 0 | 0 | D
0 | 1 | 0 | 0 | D | 0
1 | 0 | 0 | D | 0 | 0
1 | 1 | D | 0 | 0 | 0
D
S1
S1’
S0
S0’
O0 = D S 1’ S0’
O1 = D S 1’ S0
O2 = D S 1 S0’
O3 = D S 1 S0

## Slide 13: Decoders, Encoders, Priority encoders
Section - 2

## Slide 14: Decoder
A decoder is a logic circuit that accepts a set of inputs which represents a binary number and activates the only output that corresponds to the input number.
In other words, a decoder circuit looks at its inputs, determines which binary number is present there, and activates the specific output which corresponds to that number; all other outputs remain inactive.
In its general form, a decoder has N input lines to handle N bits and M output lines such that only one output line is activated for each one of the possible combinations of inputs.
I0
I1
I2
IN-2
IN-1
.
.
.
O0
O1
O2
OM-2
OM-1
.
.
.
N inputs
M outputs
Decoder
M = 2N

## Slide 15: 3-Line to 8-Line Decoder
Inputs |  |  | Outputs |  |  |  |  |  |  | 
A | B | C | D0 A’B’C’ | D1 A’B’C | D2 A’BC’ | D3 A’BC | D4 AB’C’ | D5 AB’C | D6 ABC’ | D7 ABC
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
3 to 8 line decoder can be implemented using AND gates to achieve active-HIGH output.
For active-LOW outputs, NAND gates are used.

## Slide 16
D7 = ABC
D6 = ABC’
D5 = AB’C
D4 = AB’C’
D3 = A’BC
D2 = A’BC’
D1 = A’B’C
D0 = A’B’C’
A
A’
B
B’
C
C’

## Slide 17: Encoder
Device to convert familiar numbers or symbols into coded format.
It has a number of input lines, only one of which is activated at a given time, and produces an N-bit output code depending on which input is activated.
Figure shows the block diagram of an encoder with M inputs and N outputs.
I0
I1
I2
IM-2
IM-1
.
.
.
O0
O1
O2
ON-2
ON-1
.
.
.
M inputs
N outputs
Encoder
M = 2N

## Slide 18: Priority Encoder
A priority encoder is a logic circuit that responds to just one input in accordance with some priority system, among all those that may be simultaneously HIGH.
The most common priority system is based on the relative magnitudes of the inputs; whichever decimal input is the largest, is the one that is encoded.
For example, if both decimal 3 and decimal 4 are activated simultaneously, then a priority encoder would encode decimal 4.
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | A | B | V
0 | 0 | 0 | 0 | x | x | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
x | 1 | 0 | 0 | 0 | 1 | 1
x | x | 1 | 0 | 1 | 0 | 1
x | x | x | 1 | 1 | 1 | 1

## Slide 19: Priority Encoder
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
x
1
1
1
1
1
1
1
1
1
1
1
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
x
1
1
1
1
1
1
1
1
1
A = D3 + D2
B = D3 + D2’ D1

## Slide 20: Priority Encoder
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
V = D3 + D2 + D1 + D0
D3
D2
D1
D0
B = D3 + D2’ D1
A = D3 + D2
V = D3 + D2 + D1 + D0

## Slide 21: Adders, Subtractors
Section - 3

## Slide 22: Half Adder
A combinational circuit which adds two one-bit binary numbers is called a half-adder.
The sum column resembles like an output of the XOR gate.
The carry column resembles like an output of the AND gate.
Limitations:
  In multi-digit addition we have to add two bits along with the carry of previous digit addition. Such addition requires addition of 3 bits. This is not possible in half-adders.
Inputs |  | Outputs | 
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
S = A ⊕ B
C = AB
A
B

## Slide 23: Full Adder
The full-adder adds the bits A and B and the carry from the previous column called carry-in Cin and outputs the sum bit S and the carry bit called carry-out Cout.
Inputs |  |  | Outputs | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
S = A’B’Cin + A’BCin’ + AB’Cin’ + ABCin
= (AB’ + A’B)Cin’ + (AB + A’B’)Cin
= (A ⊕ B)Cin’ + (A ⊕ B)’Cin
= A ⊕ B ⊕ Cin
Cout = A’BCin + AB’Cin + ABCin’ + ABCin
= AB + (A ⊕ B)Cin

## Slide 24: Full Adder – Logical Diagram
A
B
Cin
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin
Half Adder
Half Adder
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin

## Slide 25: Half Subtractor
Subtracts one bit from the other and produces the difference.
Other output is to specify if 1 is borrowed.
Limitation:
  Half subtractor can be used only for LSB subtraction.
Inputs |  | Outputs | 
A | B | d | b
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
d = A ⊕ B
b = A’B
A
B

## Slide 26: Full Subtractor
Full subtractor is a combinational circuit with 3 inputs (A, B, bi)
Subtraction = A – B – bi
Inputs |  |  | Outputs | 
A | B | bi | d | b
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
d = A’B’bi + A’Bbi’ + AB’bi’ + ABbi
= (AB’ + A’B)bi’ + (AB + A’B’)bi
= (A ⊕ B)bi’ + (A ⊕ B)’bi
= A ⊕ B ⊕ bi
b = A’B’bi + A’Bbi’ + A’Bbi + ABbi
= A’B(bi + bi’) + (AB + A’B’)bi
= A’B + (A ⊕ B)’bi

## Slide 27: Full Subtractor – Logical Diagram
A
B
bi
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi

## Slide 28: Binary Parallel Adder
FA3
B3
A3
S3
C3
FA2
B2
A2
S2
C2
C1
FA1
B1
A1
S1
Cin
FA4
B4
A4
S4
C4
Example: A = 1010, B = 1101
A4 A3 A2 A1 = 1010
B4 B3 B2 B1 = 1101
0
0
0
1
1
1
1
1
0
1
0
1
0
1
0
1
0

## Slide 29: Binary Parallel Subtractor
FA4
S4
Cout
B4
A4
FA3
S3
C3
B3
A3
Cin= 1
FA1
S1
C1
B1
A1
FA2
S2
C2
B2
A2
Example: A = 1101, B = 1011
A4 A3 A2 A1 = 1101
B4 B3 B2 B1 = 1011
1
1
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
0
1

## Slide 30: Binary Adder-Subtractor
FA4
S4
C4
B4
A4
FA3
S3
C3
B3
A3
FA2
S2
C2
B2
A2
FA1
S1
C1
Cin
B1
A1
When M = 0, Circuit is an adder.
When M = 1, Circuit becomes a subtractor.
M
M | Bi | O/P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 31: Digital Comparator
Section - 4

## Slide 32: Comparators
A comparator is a logic circuit used to compare the magnitudes of two binary numbers.
Comparator circuit provides 3 outputs
  A = B
  A > B
  A < B
X-NOR gate is a basic comparator (the output is 1 if and only if the input bits coincide).
2 binary numbers are equal if and only if all their corresponding bits coincide.
E.g. A3A2A1A0 and B3B2B1B0 are equal if and only if A3=B3, A2=B2, A1=B1 and A0=B0
Equality = (A3B3) (A2B2) (A1B1) (A0B0)

## Slide 33: 1-bit Magnitude Comparator
Let the 1-bit numbers be A = A0 and B = B0
If A0 = 1 and B0 = 0 then A > B
A > B : G = A0B0’
If A0 = 0 and B0 = 1 then A < B
A < B : L = A0’B0
If A0 = 1 and B0 = 1 (coincides) then A = B
A = B : E = A0 B0
A0 | B0 | L | E | G
0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
A0
B0
A < B(L)
A = B(E)
A > B(G)

## Slide 34: 2-bit Magnitude Comparator
Let the two 2-bit numbers be A = A1A0 and B = B1B0
If A1 = 1 and B1 = 0, then A > B or
If A1 and B1 coincide and A0 = 1 and B0 = 0, then A > B.
A > B : G = A1B1’ + (A1 ⊙ B1) A0B0’
If A1 = 0 and B1 = 1, then A < B or
If A1 and B1 coincide and A0 = 0 and B0 = 1, then A < B.
A < B : L = A1’B1 + (A1 ⊙ B1) A0’B0
If A1 and B1 coincide and if A0 and B0 coincide then A = B.
A = B : E = (A1 ⊙ B1)(A0 ⊙ B0)

## Slide 35: 2-bit Magnitude Comparator
A0
B0
A1
B1
A1
B1’
A0
B0’
A0’
B0
B1
A1’
A < B(L)
A = B(E)
A > B(G)

## Slide 36: Parity Generator
Section - 5

## Slide 37: Parity Generator
Binary data, when transmitted and processed is susceptible to noise that can alter its 1s to 0s and 0s to 1s.
To detect such errors, an additional bit called parity bit is added to the data bits and the word containing the data bits and the parity bit is transmitted.
At the receiving end the number of 1s in the word received are counted and the error, if any, is detected.
0 | 0 | 1 | 1
0 | 0 | 1 | 0
Even Parity
Odd Parity
Data
Data
Parity bit
Parity bit

## Slide 38: 3-bit parity generator using even parity bit
Inputs |  |  | Outputs parity bit (f)
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
AB
C
00
10
0
1
01
11
1
1
1
1
A
B
C
f

## Slide 39: Code Converters
Section - 6

## Slide 40
4-bit Binary |  |  |  | 4-bit Gray |  |  | 
B4 | B3 | B2 | B1 | G4 | G3 | G2 | G1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Binary to Gray Code Converter

## Slide 41: Binary to Gray Code Converter
K-Map for G4, G3, G2, G1 function and their minimization are as follows:
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
G3 = B4’B3 + B4B3’ = B4 B3
G4 = B4

## Slide 42: Binary to Gray Code Converter
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
G1 = B2’B1 + B2B1’ = B2 B1
G2 = B3’B2 + B3B2’ = B3 B2

## Slide 43: Binary to Gray Code Converter
Logic diagram for binary to Gray code converter is as follows:
B4
B3
B2
B1
G4
G3
G2
G1
G3 = B4’B3 + B4B3’ = B4 B3
G4 = B4
G1 = B2’B1 + B2B1’ = B2 B1
G2 = B3’B2 + B3B2’ = B3 B2

## Slide 44: BCD to Excess-3 Code Converter
8421 BCD |  |  |  | XS - 3 |  |  | 
B4 | B3 | B2 | B1 | X4 | X3 | X2 | X1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0

## Slide 45: BCD to Excess-3 Code Converter
K-Map for X4, X3, X2, X1 function and their minimization are as follows:
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
x
x
x
1
1
1
1
1
1
1
1
X3 = B3B2’B1’ + B3’ B1 + B3’ B2
X4 = B4 + B3B2 + B3B1
x
x
x
x
x
x
x
x
x

## Slide 46: BCD to Excess-3 Code Converter
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
x
x
x
1
1
1
1
1
1
1
1
X1 = B1’
X2 = B2’B1’ + B2B1
x
x
x
x
x
x
x
x
x

## Slide 47: BCD to Excess-3 Code Converter
Logic diagram for a BCD to Excess-3 is as follows
B3
B2
B1
B2’
B1’
B1
B2
X2
X4
B4
B3
B3’
B2
X3
B3
B3’
B2’
B1’
B1
X1
B1’

## Slide 48: Thank You